## Slide 1: Monte Carlo Synthetic Acceleration as Approximate Polynomial Preconditioning
Steven Hamilton
Tom Evans
Stuart Slattery
Oak Ridge National Laboratory

## Slide 2: Motivation
As we move towards exascale computing, the rate of errors is expected to increase dramatically
Algorithms need to not only have increased concurrency/scalability but have the ability to recover from faults

## Slide 3: Towards Exascale Concurrency and Resiliency
Two basic strategies:
  Start with current “state of the art” methods and make incremental modifications to improve scalability and fault tolerance
  Start with methods with natural scalability and resiliency features and work at improving performance
    One possibility: Monte Carlo

## Slide 4: Synthetic Acceleration
Nomenclature from particle transport community
No formal definition, typically refers to acceleration (preconditioning) of fixed point iteration with low order approximation of problem
Initial Richardson iteration is crucial (smoothing)
Examples: DSA, TSA, S2SA

## Slide 5: Monte Carlo Synthetic Acceleration (MCSA)
Standard synthetic acceleration algorithm, but use Monte Carlo process as preconditioner
Unlike particle transport Monte Carlo algorithms, random walks are purely algebraic rather than physics-based
Based on Halton’s sequential Monte Carlo algorithm for linear systems

## Slide 6: Adjoint Monte Carlo
Want to solve linear system Ax=b
Use Neumann series expansion of solution:
  Converges if ρ(H)<1
Decompose adjoint of H into element-wise product of transition probability matrix (P) and weight matrix (W):
  Typically rows of P chosen to be probability distribution functions with magnitudes based on elements in row of HT

## Slide 7: Preconditioning
H formed from Richardson iteration on preconditioned system:
We require explicit representation for preconditioned matrix
  Sparsity of preconditioner does not imply sparsity of H
  Developing preconditioners resulting in sparse H is an area for future work

## Slide 8: Example
Suppose history current resides in state 3
  20% chance of transition to state 1, 80% chance to state 2
  Weight of history multiplied by 0.5
  Solution updated by: xi = xi + w

## Slide 9: Starting and stopping random walk
To determine the initial state and weight of particle, sample right hand side vector:
  In MCSA, b is the residual corresponding to the current iterate: more particles started in locations where residual is large
Terminate history when particle weight decreases by prescribed amount:

## Slide 10: Previous Success with MCSA
Evans, Mosher, Slattery, Hamilton, “A Monte Carlo Synthetic-Acceleration Method for Solving the Thermal Radiation Diffusion Equation,” JCP 258 (2014)
Radiation diffusion Marshak wave problem
  Transient 100ns in duration
Solver | Total Iterations | Relative Time Per Iteration | Relative Total Time
CG (ML) | 12150 | 74.7 | 2.7
GMRES (ILU) | 40294 | 103.0 | 9.2
MCSA (Jacobi) | 98863 | 1.0 | 1.0

## Slide 11: Weight vs. History Length Cutoff
JPWH_991 matrix from Matrix Market
MCSA w/diagonal preconditioning (ρ(I-D-1A)≈0.98)
Statistically noisy approximation to full Neumann series far worse than good approximation to a few terms
Iteration Count to Convergence |  |  |  |  | 
 | Weight Cutoff |  | History Length Cutoff |  | 
# Histories | 1e-4 | 0.5 | 10 | 20 | 40
100 | - | - | 269 | 356 | -
400 | 232 | 234 | 56 | 186 | 220
1600 | 206 | 200 | 57 | 31 | 179
6400 | 185 | 169 | 57 | 32 | 16
25600 | 159 | 128 | 57 | 31 | 17

## Slide 12: Weight vs. History Length Cutoff
JPWH_991 matrix from Matrix Market
MCSA w/diagonal preconditioning (ρ(I-D-1A)≈0.98)

## Slide 13: Weight vs. History Length Cutoff
JPWH_991 matrix from Matrix Market
MCSA w/diagonal preconditioning (ρ(I-D-1A)≈0.98)
Statistically noisy approximation to full Neumann series far worse than good approximation to a few terms

## Slide 14: Truncated Neumann Series
Terminating Neumann series after relatively small number of terms leads to better statistical behavior
Monte Carlo process approximates application of Neumann series polynomial to a vector
Why stop with Neumann series?
Monte Carlo tally: xi = xi + cmw
Contribution to solution depends on current “stage” in history

## Slide 15: Polynomial Preconditioning
Choose polynomial pn(x) such that pn(A)≈A-1
Typically desirable to make I-pn(A)A “small”
One approach: let qn+1(A)=I-pn(A)A, choose qn+1 such that
  qn+1 is the Chebyshev polynomial Tn+1(αI+βA)
  α,β related to extremal eigenvalues of A

## Slide 16: Neumann vs. Chebyshev Polynomials
For given polynomial order, Chebyshev polynomials result in much lower iteration count
Far more histories required for stability
  Chebyshev coefficients increase exponentially
Iteration Counts to Convergence |  |  |  |  |  |  |  | 
 | Neumann Polynomial Order |  |  |  | Chebyshev Polynomial Order |  |  | 
# Histories | 5 | 10 | 20 | 40 | 1 | 2 | 3 | 4
250 | 96 | 48 | 216 | 251 | 143 | - | - | -
1000 | 99 | 57 | 29 | 194 | 126 | - | - | -
4000 | 98 | 57 | 32 | 48 | 124 | 64 | - | -
16000 | 97 | 57 | 31 | 17 | 123 | 63 | 38 | -
64000 | 97 | 57 | 31 | 17 | 122 | 63 | 39 | -
256000 | 97 | 57 | 31 | 17 | 122 | 63 | 39 | 27

## Slide 17: Neumann vs. Chebyshev Polynomials
For comparison, GMRES(10) with same preconditioner took 70 iterations and relative timing of 1.5
Relative Timing to Convergence |  |  |  |  |  |  |  | 
 | Neumann Polynomial Order |  |  |  | Chebyshev Polynomial Order |  |  | 
# Histories | 5 | 10 | 20 | 40 | 1 | 2 | 3 | 4
250 | 2.4 | 1.0 | 2.6 | 3.0 | 1.4 | - | - | -
1000 | 2.6 | 2.4 | 2.6 | 3.4 | 2.5 | - | - | -
4000 | 4.5 | 4.5 | 3.6 | 4.4 | 6.8 | 5.1 | - | -
16000 | 8.4 | 8.4 | 8.1 | 6.8 | 23.9 | 19.4 | 15.1 | -
64000 | 15.8 | 16.1 | 17.0 | 11.4 | 93.9 | 74.0 | 64.1 | -
256000 | 31.1 | 32.3 | 33.6 | 33.8 | 365.6 | 292.1 | 256.3 | 228.9

## Slide 18: SPN Equations
SPN approximation to Boltzmann neutron transport equation
Series of coupled diffusion equations (moment and energy)
More accurate than standard diffusion approximation for nuclear reactor problems, easier to solve than transport

## Slide 19: Reactor Assembly Problem
2601 mesh cells
  3x3 array of assemblies in 2D
  Each assembly is 17x17 array of fuel pins
  1 mesh cell per pin
  Homogenized cross sections
23 energy groups
SP3 (2 moment equations)
120k total unknowns, 6.8M nonzeros
Δt=10-6
Block diagonal preconditioning
  Block size is number of energy groups
  ρ(H)=0.99

## Slide 20: Reactor Assembly Results
Similar behavior as simpler problem
  More histories required for stability (larger dimension and higher spectral radius)
Iteration Counts to Convergence |  |  |  |  |  | 
 | Neumann Polynomial Order |  |  | Chebyshev Polynomial Order |  | 
# Histories | 5 | 10 | 20 | 1 | 2 | 3
25k | 347 | 376 | - | - | - | -
50k | 286 | 106 | 464 | - | - | -
100k | 178 | 104 | 364 | 300 | - | -
200k | 175 | 103 | 62 | 260 | - | -
400k | 174 | 102 | 59 | 250 | - | -
800k | 174 | 102 | 58 | 250 | - | 453
1.6M | 174 | 102 | 57 | 251 | - | 77

## Slide 21: Reactor Assembly Results
GMRES approximately factor of 5 faster than best case (124 iterations)
Relative Timing to Convergence |  |  |  |  |  | 
 | Neumann Polynomial Order |  |  | Chebyshev Polynomial Order |  | 
# Histories | 5 | 10 | 20 | 1 | 2 | 3
25k | 1.3 | 1.2 | - | - | - | -
50k | 1.6 | 1.0 | 2.2 | - | - | -
100k | 3.1 | 2.2 | 2.7 | 2.0 | - | -
200k | 6.2 | 4.8 | 1.9 | 3.7 | - | -
400k | 13.9 | 10.5 | 4.6 | 6.4 | - | -
800k | 27.1 | 22.9 | 10.1 | 12.3 | - | 12.1
1.6M | 49.2 | 45.7 | 22.4 | 23.1 | - | 13.7

## Slide 22: Parallel Performance

## Slide 23: Conclusions
Truncating Neumann series leads to improved statistical behavior in adjoint Monte Carlo process
  Better iterative convergence with fewer histories in MCSA algorithm
Replacing Neumann series with Chebyshev polynomials can further reduce iteration counts
  Statistical properties far worse than Neumann series
  Not currently competitive, may change with parallelism

## Slide 24: Difficulties, Opportunities, Future Work
Spectral radius must be less than 1
  Preconditioning while maintaining sparsity
Alternate polynomials to approximate A-1
  Better convergence than Neumann, better statistical behavior than Chebyshev
  GMRES polynomial?
Hybrid parallelism
  Good scaling in both MPI and OpenMP individually
  Possibly overlapping additive Schwarz, minimal communication
  Strong potential for GPU, Xeon Phi

## Slide 25: Acknowledgements
Funding for this work was provided by a DOE Advanced Scientific Computing Research (ASCR) grant
This work was authored by UT-Battelle, LLC, under Contract No. DE-AC05-00OR22725 with the US Department of Energy.